## Slide 1: Definitions.
Definitions. Before we can discuss control systems, some basic terminologies must be defined.
The controlled variable is the quantity or condition that is measured and controlled.
The control signal or manipulated variable is the quantity or condition that is varied by the controller so as to affect the value of the controlled variable. Normally, the controlled variable is the y(t) output of the system.
Control means measuring the value of the controlled variable of the system and applying the control signal to the system to correct or limit deviation of the measured value from a desired value.

## Slide 2: Definitions.
Plants. A plant may be a piece of equipment, perhaps just a set of machine parts functioning together, the purpose of which is to perform a particular operation. In this book, we shall call any physical object to be controlled (such as a mechanical device, a heating furnace, a chemical reactor, or a spacecraft) a plant.
Processes. The Merriam–Webster Dictionary defines a process to be a natural, progressively continuing operation or development marked by a series of gradual changes that succeed one another in a relatively fixed way and lead toward a particular result or end; or an artificial or voluntary, progressively continuing operation that consists of a series of controlled actions or movements systematically directed toward a particular result or end. In this book we shall call any operation to be controlled a process. Examples are chemical, economic, and biological processes.

## Slide 3: Definitions.
Systems. A system is a combination of components that act together and perform a certain objective. A system need not be physical. The concept of the system can be applied to abstract, dynamic phenomena such as those encountered in economics. The word system should, therefore, be interpreted to imply physical, biological, economic, and the like, systems.
Disturbances. A disturbance is a signal that tends to adversely affect the value of the output of a system. If a disturbance is generated within the system, it is called internal, while an external disturbance is generated outside the system and is an input.
Feedback Control. Feedback control refers to an operation that, in the presence of disturbances, tends to reduce the difference between the output of a system and some reference input and does so on the basis of this difference. Here only unpredictable disturbances are so specified, since predictable or known disturbances can always be compensated for within the system.

## Slide 4: EXAMPLES OF CONTROL SYSTEMS
Watt’s speed governor for an engine

## Slide 5: EXAMPLES OF CONTROL SYSTEMS
Temperature Control System.

## Slide 6: Classification of models
Materiell modells are:
- Geometric modells (Sample)
- Experimental modells
+ Natural modells
+ Künstliche modells
- Educational (exhibitional modells)
- Research (experimental modells)
Abstrackted modells are:
- Geometric construction modells (CAD)
- Physical modells
+ Kontinuum- modells
+ Diskret - modells
- Mathematic models