## Slide 1
Vehicle Informatics
(Vehicle System Informatics)
Flexray
Dr. Tamás Szakács: szakacs.tamas@bgk.uni-obuda.hu,
Ákos Jányoki: janyoki.akos@bgk.uni-obuda.hu

## Slide 2
FlexRay
Advanced Automotive Communication System
Outline:
Scalable static and dynamic message transmission (deterministic and flexible)
High net data rate of 5 Mbit/sec; gross data rate approximately 10Mbit/sec
Scalable fault-tolerance (single and dual channel)
Error containment on the physical layer through an independent Bus Guardian
Fault tolerant clock synchronisation (global time base)

## Slide 3
FlexRay
Demand for a bus system with high data rate
Deterministic and fault tolerant bus system for advanced automotive control
applications
Support from the bus system for distributed control systems
Limited number of different communication systems within vehicles
Motivation
requirements
telematics
control systems
LIN
CAN
MOST
FlexRay

## Slide 4
Goals
Develop an advanced communication technology for high-speed control applications in vehicles
Make the technology available in the market place for everyone
Drive the technology as a defacto standard
FlexRay

## Slide 5
Synchronous and asynchronous data transmission (scalable)
High net data rate of 5 Mbit/sec; gross data rate approximately 10Mbit/sec
Deterministic data transmission, guaranteed message latency and message jitter
Support of redundant transmission channels
Fault tolerant and time triggered services implemented in hardware
Fast error detection and signalling
Support of a fault tolerant synchronised global time base
Error containment on the physical layer through an independent “Bus Guardian”
Arbitration free transmission
Support of optical and electrical physical layer
Support for bus, star and multiple star topologies
Basic Features
FlexRay

## Slide 6: Hardware Features and Topology of a Distributed FlexRay System - Active Star
Optional redundant communication channels
1 to 1 communication connections in combination with active stars
Support of “wake-up” via bus
Support of net data rates up to 5 Mbit/sec
Support of power management
ECU
Active Star
Redundancy
Physical 1 to 1 Communication Connection
Communication
Controller and µC
Bus Driver
FlexRay

## Slide 7
Hardware Features and Topology of a Distributed FlexRay System - Passive Bus
Solution with restrictions (reuse of available Physical Layer):
Optional redundant communication channels
Support of “wake-up” via bus, depends on the Physical Layer
low gross data rate (similar to CAN)
Support of power management, depends on the Physical Layer
Bus Guardian, depends on the Physical Layer
FlexRay

## Slide 8
1 or 2 bus drivers connected to one communication controller
Connection to “permanent power”
“Wake-up” via bus
“Shut-down” by the ECU
Features and Block Diagram of a FlexRay ECU
Communication Controller
Microcontroller (Host)
Power Supply
Bus
ECU
Bus
Permanent Power
Bus Driver
Bus Guardian
Bus Driver
Bus Guardian
FlexRay

## Slide 9
Power Supply
Bus
Bus
Permanent Power
More than 1 bus driver required
Communication controller and micro controller are not required
Connection to “permanent power”
“Wake-up” via bus
“Shut-down” via bus
Features and Block Diagram of a FlexRay Active Star
Active Star
Bus Driver
Bus Driver
FlexRay

## Slide 10
Data Transmission
frame
(static part)
frame
(dynamic part)
communication cycle
1
2
3
4
5
6
7
8
9
A
da
B
db
C
dc
B
dd
D
de
E
df
F
dg
C
dk
10
static part
dynamic part
1
2
3
4
5
6
7
8
9
A
d´a
B
dh
C
di
G
dj
C
d´k
10
messages channel 2
0
0
B
d´d
D
d´e
11
11
A
d´l
A
dl
12
12
A
dn
A
dm
13
G
dp
13
14
F
do
15
E
dq
14
15
...
...
ID
datatype
ID
datatype
messages channel 1
1
2
3
4
5
6
7
9
1
2
3
8
9
4
5
11
11
12
12
13
14
15
slot
slot
sync symbol
node B
node C
node D
node E
node F
node G
node A
channel 1
channel 2
node
node
FlexRay

## Slide 11
FlexRay Protocol Frame Format (I)
ID: Identifier, 10 bit, range: (110 ... 102310), defines the slot number in the static part or the priority in the dynamic part
MUX: Multiplex Field, 1 bit, enables a node to transmit different messages with the same ID
SYNC: Synchronisation Field, 1 bit, tags the frames which will be used for the clock synchronisation
LEN: Length field, 4 bit, LEN = number of used data bytes (010 ... 1210)
D0 ... D11:Data bytes, 0-12 bytes
CRC: Cyclic Redundancy Check Field, 16 bit
FlexRay

## Slide 12
FlexRay Protocol Frame Format (II)
The cycle counter will be used to synchronise application processes which
are longer as the communication cycle.
CYCLE: Cycle Counter, 8 bit, range: (010 ... 25510). The CYCLE-field will be used as cycle counter or as a data byte. The cycle counter will be incremented consistently in all communication controllers at the beginning of each communication cycle
SYNC: Synchronisation field, 1 bit, tags the frames which contain the cycle counter
D0 ... D10: Data bytes, 0-11 bytes
FlexRay

## Slide 13
FlexRay Protocol Clock Synchronisation
Synchronisation of the local clocks to a global time base
Up to two asymmetric faults can be tolerated if there are a sufficient number of nodes
Fault tolerant clock synchronisation is available in a pure static configuration and in a mixed configuration (static and dynamic part in the communication cycle)
No fault tolerant clock synchronisation is available in a pure dynamic configuration
Support of all topologies (single channel, dual channel, mixed single and dual channel)
Only nodes in the static part can participate in the clock synchronisation
(with frames which are tagged with the SYNC bit)
All nodes can use the global time
FlexRay

## Slide 14
Market
  Trends in the information society
    Computerized components for mechanical engineering
    Aircraft domain (Airbus A320)
  Who can make it possible for cost-sensitive industry?
    Automobile, industrial control, and so on
TTTech – Time Triggered Technology
  Offer products for evaluation and design of TTP-based system
Why Time-Triggered Protocol
TimeTriggeredProtocol.ppt

## Slide 15
TTP – more than just a protocol
  Network protocol
  Operating system scheduling philosophy
  Fault tolerance approach
Time-Triggered approach
  Stable time base
  Simple to implement the usual stuff
  Cyclic schedules
TTP (Time-Triggered Protocol)
TimeTriggeredProtocol.ppt

## Slide 16
TTP/A (Automotive Class A = soft real time)
  A scaled-down version of TTP
  A cheaper master/slave variant
TTP/C (Automotive Class C = hard real time)
  A full version of TTP
  A fault-tolerant distributed variant
Two derivation
TimeTriggeredProtocol.ppt

## Slide 17
For example: How do you do this for about $2 per node?
  Answer: after making compromises, … and use on Class A devices (soft real time)
  Distributed fault tolerance is expensive (especially time bases), so go master/slave polling instead
TTP/A: A reduced cost version
TimeTriggeredProtocol.ppt

## Slide 18
Protocol Layer in TTP/A
TimeTriggeredProtocol.ppt

## Slide 19
Operation
  Master polls the other nodes (slaves)
  Non-master nodes transmit messages when they are polled
  Inter-slave communication through the master
Polling
TimeTriggeredProtocol.ppt

## Slide 20
Advantage
  Simple protocol to implement
  Historically very popular
  Bounded latency for real-time applications
Disadvantage
  Single point of failure from centralized master
  Polling consumes bandwidth
  Network size is fixed during installation(or master must discover nodes during reconfiguration)
Poll Tradeoff
TimeTriggeredProtocol.ppt

## Slide 21
TTP/C
  A time-triggered communication protocol for safety-critical (fault-tolerant) distributed real-time control systems
  Based on a TDMA(Time Division Multiple Access) media access strategy
  Based on clock synchronization
TTP/C
TimeTriggeredProtocol.ppt

## Slide 22
Some Concepts
CNI
  Communication Network Interface: interface between communication controller and the host computer within a node of a distributed system
Composability
  various components of a software system can be developed independently and integrated at a late stage of software development
Fail Silence
  A subsystem is fail-silent if it either produces correct results or no results at all, i.e., it is quiet in case it cannot deliver the correct service
FTU
  Fault-Tolerance Unit
SRU
  Smallest Replaceable Unit
TTP/C
TimeTriggeredProtocol.ppt

## Slide 23
Application software in Host
FTU Membership
Redundancy Management
SRU Membership
Clock Synchronization
Media Access: TDMA
Host Layer
FTU CNI
FTU Layer
RM Layer
SRU Layer
Data Link/Physical Layer
Basic CNI
TTP/C Protocol Layer
TimeTriggeredProtocol.ppt

## Slide 24
(Contd.)
Data Link/Physical Layer
  Provide the means to exchange frames between the nodes
SRU Layer
  Store the data fields of the received frames
RM Layer
  Provide the mechanisms for the cold start of a TTP/C cluster
FTU Layer
  Group two or more nodes into FTUs
Host Layer
  Provide the application software
Basic CNI
  A data-sharing interface between the RM layer and FTU layer
FTU CNI
  The interface between FTU layer and Host Layer
TimeTriggeredProtocol.ppt

## Slide 25
Precise Interface Specifications
Composability
Reusability of Components
Improved Supplier/Sub-supplier Relationship
Timeliness
Error Containment
Constructive Testability
Seamless Integration of Fault-Tolerance
Simpler Application Software
Shorter Time-to-Market
Reduced Development Costs
Reduced Maintenance Costs
Objectives in TTP/C
TimeTriggeredProtocol.ppt

## Slide 26
Structure of TTP/C System
TimeTriggeredProtocol.ppt

## Slide 27
Two active nodes, two shadow nodes
Three active nodes with one shadow nodes (Triple modular Redundancy)
Two active nodes without a shadow node
FTU Configuration Examples
FTU in TTP/C
TimeTriggeredProtocol.ppt

## Slide 28
Includes controller to run protocol
DPRAM (dual ported RAM)
  To implement memory-mapped network interface
BG (Bus Guard)
  Hardware watchdog to ensure “fail silent”
Real chips must use highly accurate time sources
  Even dual redundant crystal oscillators as used in DATAC for Boeing 777)
Single Node Configuration
TimeTriggeredProtocol.ppt

## Slide 29
Single Node Configuration
TTP/C
TimeTriggeredProtocol.ppt

## Slide 30
TDMA Cycle
  One FTU sends results twice
  Then next FTU sends some results
  And so on, until back to the next message from the first FTU
Cluster Cycle
  Cluster cycle involves scheduling all possible message and tasks
Cycle in TTP/C
TimeTriggeredProtocol.ppt

## Slide 31
I-Frames used for initialization
N-Frames used for normal messages
TTP/C Frame
TimeTriggeredProtocol.ppt

## Slide 32
Advantage
  Simple protocol to implement
  Deterministic response time
  No wasted time for Master polling message
Disadvantage
  Single point of failure from the bus master
  Wasted bandwidth when some nodes are idle
  Stable clocks
  Fixed network size during installation
Pros and Cons of TTP
TimeTriggeredProtocol.ppt

## Slide 33
Service
TTP/A
TTP/C
Clock Synchronization
Central
Multimaster
Distributed,
Fault-Tolerant
Mode Switches
yes
yes
Communication Error Detection
Parity
16/24 bit CRC
Membership Service
simple
full
External Clock Synchronization
yes
yes
Time-Redundant Transmission
yes
yes
Duplex Nodes
no
yes
Duplex Channels
no
yes
Redundancy Management
no
yes
Shadow Node
no
yes
A comparison TTP/A vs. TTP/C

## Slide 34
TTP/A is intended for low cost
TTPnode implements such an integrated TTP/C and TTP/A solution to carry out all sensing and actuating action within hard real-time deadlines and minimal jitter
(Jitter: The jitter is the difference between the maximum and the minimum duration of an action (processing action, communication action) )
TTP/C + TTP/A
TimeTriggeredProtocol.ppt

## Slide 35
TTTech Evaluation Cluster -- TTP Hardware Systems
  TTP Hardware Products
    TTPnode
  TTP Software Products – TTP tools
    TTPplan
    TTPbuild
    TTPos
    TTPView
    TTPload
TTTech – Time Triggered Technology
TimeTriggeredProtocol.ppt

## Slide 36
TTP Evaluation Cluster

## Slide 37
TTPnode

## Slide 39
(Contd.)
TTPplan
A comprehensive tool for the design of TTP clusters based on the concepts of state messages and temporal firewalls
TTPbuild
An environment for the design of nodes in a TTP cluster
TTPos
The Time-Triggered Architecture and the TTP/C communication protocol, with fault-tolerance
TTPview
An easy-to-use graphical user interface which monitors the real-time messages among nodes
TTPload
An easy-to-use graphical user interface which allows to create and maintain download collections

## Slide 40: Demonstration
Specification
  Controller and cluster communication startup
  Basic communication with TTP/C
  Basic FT layer features like host lifesign and message handing
  Building a replica determinate task
  Re-integration of a replica using h-state messages
  Checking the current degree of redundancy of a message
  Reacting to sporadic events in a time-triggered architecture
TTP