## Slide 1: Programmable control systems
The first ones was introduced in the late 1960’s
Before that we had relay logic circuits which were hard wired

## Slide 2: Programmable control systems
As technology quickly progressed, many complex operational tasks have been solved by connecting programmable logic controllers (PLC) and a central computer. Beside connections with devices, possibilities for communication among instruments are so great that they allow a high level of exploitation and process coordination.
With the execution of a program stored in program memory, PLC continuously monitors status of the system through signals from input devices. Based on the logic implemented in the program, PLC determines which actions need to be executed with output instruments. To run more complex processes it is possible to connect more PLC controllers to a central computer

## Slide 3: Advantages of control panel that is based on a PLC controller:
1. number of wires needed for connections is reduced by 80%
2. Consumption is greatly reduced
3. allow for fast and easy error detection.
4. Change in operating sequence or application of a PLC controller to a different operating process can easily be accomplished
5. Needs fewer spare parts
6. It is much cheaper compared to a conventional system
7. Reliability of a PLC is greater than that of an electro-mechanical relay or a timer

## Slide 4: Where is PLC used and why?
First used by automotive
  Hard wired relays were complicated, expensive, unreliable
Lots of I/O
  Many components are controlled
Stability/ Reliability
  Designed for the industry
  Compared to PC, this can not crash
Home automation
  Very easy to program
  Visual programming

## Slide 5: Types of PLCs
Small system – less than 500 I/Os.
Medium system has I/Os ranging from 500 to 5,000.
Large system with over 5,000 I/Os

## Slide 6: Types of PLCs

## Slide 7: Port selection, modules
Start
Stop
Init
Output
Input

## Slide 8: PLC programming languages
Ladder diagram (LD)
Sequential Function Charts (SFC)
Function Block Diagram (FBD)
Structured Text (ST)
Instruction List (IL)

## Slide 9: Process of a scan cycle
Input Scan:
  A simple way of looking at this is the PLC takes a snapshot of the inputs and solves the logic
Execute Program (or Logic Execution):
  The PLC executes a program one instruction at a time using only the memory copy of the inputs the ladder logic program
Output Scan:
  When the ladder scan completes, the outputs are updated using the temporary values in memory

## Slide 10: Solenoid valves
A solenoid valve is an electromechanically operated valve.

## Slide 11: Relay

## Slide 12: Reed Relay
It is a type of relay that uses an electromagnet to control one or more reed switches.
The contacts are of magnetic material and the electromagnet acts directly on them without requiring an armature to move them

## Slide 13: Shift Register

## Slide 15: In Lab
H10 single acting (monostable); H11 double acting cylinder (bistable)
1
2
3
H4
H5
H6
H1
H7
H2
H3
H9
H8
H10
H11

## Slide 16
16
D112
D111
D111 (000.06)
D102 (000.05)
D101 (000.04)
H11
H10
START
1
2
3
4
1 Working cyclic
D112 (000.07)
Physical Model PLC
D102 ΔT
D101